Wireless Multimedia Systems Fall, 2003

(Oct 13, 2004)

- Today's topic:

II. Propagation and Radio System Design Issues in Mobile Radio Systems

Frequency Reuse, The Cellular Concept

(A) Theodore S. Rappaport, Keith Blankenship, Hao Xu, “Propagation and Radio System Design Issues in Mobile Radio Systems for the GloMo Project”, 1997

(B) Wireless and Mobile System Chapter 3

(C) The Cellular Concept

I. From a T-R transceiver point of view: (SNR)

- Large Scale Path Loss Model (Link Budget Design)

Signal:

Frequency: Lower frequency has less Path loss than higher frequency

Exercise 1: (Power Issue & Link Budget)

Maximum separation distance vs. transmitted power (with fixed BW)

•Given

Cellular phone with 0.6W transmitted power

Unity gain antenna, 900 MHz carrier frequency

SNR must be at least 25 dB for proper reception

Receiver BW is B=30KHz, noise figure F=10 dB

•What will be the maximum distance?

•Solution:

N= -174 dBm + 10 log 30000 + 10 dBM

For SNR > 25 dB, we must have Pr > (-119+25) = -94 dBm

Pt=0.6W = 27.78 dBm

This allows path loss PL(d) = Pt – Pr < 122 dB

( = c/ f = 1/3 m

Assuming d0 = 1 km, PL (d0) = 91.5 dB

for free space,

n=2, so that : 122 > 91.5 + 10 * 2 log (d / 1 km) )

so  d < 33.5 km,

for shadowed urban with

n=4,  so that  122 > 91.5 + 10*2*log (d/1km))

so  d < 5.8 km

- The noise Level (N=-174(dBm)+10log10B+F(dB)) vs BW

Usually, More bandwidth brings more noise.

- Battery, Transmitted Power, Distance

More power will go for more distance. Battery life will get less.

Free space (n=2) will have more distance than shadow (N=4)

(c) Bandwidth, Transmitted Power, Battery

More bandwidth will bring more noise and require more transmitted power.

- From a system point of view

- SIR (Signal to Interference Ratio, co-channel interference),

The cellular Concept/Frequency Reuse:

The same frequency will be reuse at the reuse distance D. (Co-Channel Interference)

N= 1, 3, 4, 7, 9, 12……

e.g.

  - n=4

  - 2. worst case is at D0 = R (when MH is at the fringe of its cell)

  - 3. only the six “first-tier” co-channel cells are considered

  - 4. D1 = D2 = D3 = D4= D5 = D6 =  D

| system | (C/I)min | D/R | N |
| --- | --- | --- | --- |
| AMPS | 18 dB | 4.6 | 7 |
| GSM | 11 dB | 3.0 | 4 |