Wireless Multimedia Systems Fall, 2004 (Nov 3, 2004)

- Today's topic:

Finishing 802.11/Bluetooth

Cellular Concepts: Channel Assignments and Handoff”

Suggested Reading:

Required Reading:

- [Katzela96]Katzela, and M. Nahgshineh,”Channel assignment schemes for cellular mobile telecommunication systems: a comprehensive survey,” IEEE Personal Communications, June 1996

- [Pollinin96], G.P. Pollini, “Trends in handover design, “IEEE Communications Magazine, March 1996

- Overviews:

(1) Demand Growth: (a) the Ubiquitous information access (b) increasing number of users (c) multimedia bandwidth demanding

(2) Challenges of Cellular Technologies:

(a) Efficient reuse of the scarce radio spectrum: Interference issues (e.g. co-channel interferences and proper channel assignments for different traffic demanding)

(b) Continuous QoS provisions: (handoff)

- Channel Allocation Schemes (Channel Assignment Schemes)

(1) Channel Resources (FD (Frequency Division), TD (Time Division), CD (Code Division)

(2) Co-Channel: the same set of channels can be reused at a minimum distance (co-channel reuse distance) to maintain CIR (Carrier signal over co-channel interference)

(3) Fixed Channel Allocation (Fixed Channel Assignment)

Assign a number of channels to each cell according to some reuse pattern

(4) Dynamic Channel Allocations (Dynamic Channel Assignment)

All channels are placed in a pool and assigned to a new call to satisfy minimum CIR

(5) Flexible Channel Allocations

- Handling Handoffs

Performance Metrics: Call blocking prob, Handoff blocking prob, Interruption, delay

Handoff initiations: relative signal strength, with threshold, with hysteresis, Prediction

SIR measurement by network controlled, mobile assisted, mobile-control handoff

Macrocell/Microcell Overlays: velocity estimation, multi-tier control, integrated system, teletraffic

- More Schemes:

Reuse Partitioning: (RUP): each cell is divided into two or more concentric subcells

Overlapping Cells

Power Control

Bluetooth (802.15 for short range communications, Personal Area Network)

Wireless Connection is established in an Ad-hoc manner. Data delivery relies on a piconet. A piconet consists of a Master and up to 7 slaves. All devices on a piconet follow the frequency hopping sequence and timing of the master. Several piconets could be linked as a Scatternet.

<I> First Step (Service Discovery Protocol, Inquiry/Inquiry Scan), Page/Page Scan

<II> Connection Established (Time Division Multiplexing within a piconet)

ACL (Asynchronous Connection Link)

SCO (Synchronous Connection Link)

<III> Power Saving/Power Management:

Standby/Idle Mode: the unit only scans a little over 10 ms every (1.28 second to 3.84 seconds)

Hold/Park/Sniff (after the piconet has been established)

Hold: for another inquiry/scan/page functions

Sniff: low power mode, the slave scans at a larger interval

Park: it only listens to the channel at a very low duty cycle

Advanced 802.11 Management:

<I> 802.11 Power Saving

Infrastructure: TIM

Beacon Message:

Timestamp

Beacon Interval

Capability Information

SSID (Service Set Identity, ESS or IBSS)

Supported Rates

CF Parameter Set

IBSS Parameter Set

TIM

Association Request: (Capability Information, Listen Interval, SSID, Supported Rates)

Association Response: (Capability Information, Status Code, Station ID, Supported Rates)

Ad hoc (IBSS): ATIM

<II> 802.11 Handoff

Mobility

Handoff

IAPP Protocol

GPRS (General Packet Radio Service in GSM)

<I> share physical GSM resource on a dynamic flexible basis

<II>Capacity on Demand: dynamically allocate the packet data channels for each cell and allocate multiple of packet data channels for a user

Spread Spectrum Access Method for Wireless Communications (CDMA)

<I> Universal Frequency Reuse

Direct Sequence Cellular CDMA:

<II> Power Control:

Reverse Link

Forward Link

<III> Soft Handoff and Space Diversity

<IV> Cellular User Capacity to determine the allowed number of user for a CDMA cellular system