Wireless Multimedia Systems Fall, 2004 (Dec 08, 2004)

Professor Eric Hsiao-kuang Wu (hsiao@csie.ncu.edu.tw)

- Today's topic (II):

Summary of coming issues

Finishing Wireless TCP

Topic I:  Wireless TCP

Suggested Reading:

Required Reading:

- [Balakrishnan95], Harri Balakrishnan, Srinivasan Seshan, Elan Amir and Randy H. Katz, “Improving TCP/IP Performance over Wireless Networks”, ACM Mobicom95

- [Balarkrishnan97], Harri Balarkrishna, Venkat N, Padmanabhan, Srinivasan Seshan and Randy Katz, “A Comparison of Mechanisms for Improving TCP Performance over Wireless Links”, IEEE JSAC 97.

- Reference: [Mario2001], Mario Gerla, “West TCP”, Mobicom2001

- Fundamental of TCP

(1) flow control (congestion control) and error control (retransmission)

(2) slow start, congestion avoidance, time out (window size, threshold)

(3) fast retransmission

- Challenge of Wireless TCP

- Heterogeneous network (Wired and wireless)

- The mobility problem

- The wireless characteristics

- Solutions of Wireless TCP

Non-End-to-End Schemes

- Split Connection Approach

Indirect TCP (I-TCP):

An end-to-end connection between a fixed host a mobile host is split into two separate connections.

Motivation:

Mobile IP proposals attempt to hide mobility, disconnection from higher layer

Therefore host mobility causes temporary disruption

Error prone wireless links

Advantage: a more optimized wireless link-specific protocol tuned for better performance

Disadvantage:

  - Not end-to-end semantic:

  - Application relinking

  - Software overhead

- Link Layer Approach

FEC (Forward Error Correction)

ARQ (Automatic repeat request)

- Snoop Approach

The snoop agent monitors every packet that passes through the TCP connection in both directions and maintains a cache of TCP segments sent across the link that have not yet been acknowledged by the receiver.

End-to-End Schemes

- ELN Approach

Explicit Loss Notifications

- Westwood TCP