Wireless Multimedia Systems Fall, 2009 ( Lecture 4)

- Today's topic:

MAC for Multimedia Applications: Current Solutions: Bluetooth, 802.11

Suggested Reading:

Required Reading:

(Haartsen2000) Jaap C. Haartsen,”The Bluetooth Radio System”, IEEE Personal Communications, February 2000

(Xiao2002) Y. Xiao, J. Rosdhal, “Throughput and Delay Limits of IEEE 802.11”, IEEE Communications Letters, August 2002.

- MAC Requirements

Fundamental Requirements and pure traffic support (wireless data network, wireless voice network

Multimedia MAC: to carry mixed traffic over the same wireless medium (Bluetooth (ACL, SCO), 802..11 (DCF, PCF), GPRS (different QoS))

Soft-Resource (CDMA) and Dynamic bit rate

- Concerns for Multimedia Medium Access

Channel Acquisitions

Collision Free Transmission

Interference Suppression (Spread Spectrum)

- Mobile Ad hoc Network (MANET)

Evolution of Mobile Ad hoc Network

Commercial Applications of Mobile Ad hoc Network

Challenges of MANET

- Typical Multimedia Medium Access Examples:

Bluetooth (ISM 2.4 G, Frequency Hopping (FH) )

Connection Establishment: Inquiry/Inquiry Scan/Page

Transmissions: SCO, ACL, Polling

Power Saving: Park, Hold, Sniff

Implementations

802.11 (ISM 2.4 G, Direct Sequence (DS) )

DCF (Distributed Coordination Function, RTS/CTS/DATA/ACK)

PCF (Point Coordination Function, POLLING)

GPRS (General Packet Service, GSM Band)

Multiple SLOT Access

Bluetooth (802.15 for short range communications, Personal Area Network)

Wireless Connection is established in an Ad-hoc manner. Data delivery relies on a piconet. A piconet consists of a Master and up to 7 slaves. All devices on a piconet follow the frequency hopping sequence and timing of the master. Several piconets could be linked as a Scatternet.

<I> First Step (Service Discovery Protocol, Inquiry/Inquiry Scan), Page/Page Scan

<II> Connection Established (Time Division Multiplexing within a piconet)

ACL (Asynchronous Connection Link)

SCO (Synchronous Connection Link)

<III> Power Saving/Power Management:

Standby/Idle Mode: the unit only scans a little over 10 ms every (1.28 second to 3.84 seconds)

Hold/Park/Sniff (after the piconet has been established)

Hold: for another inquiry/scan/page functions

Sniff: low power mode, the slave scans at a larger interval

Park: it only listens to the channel at a very low duty cycle

Advanced 802.11 Management:

<I> 802.11 Power Saving

Infrastructure: TIM

Beacon Message:

Timestamp

Beacon Interval

Capability Information

SSID (Service Set Identity, ESS or IBSS)

Supported Rates

CF Parameter Set

IBSS Parameter Set

TIM

Association Request: (Capability Information, Listen Interval, SSID, Supported Rates)

Association Response: (Capability Information, Status Code, Station ID, Supported Rates)

Ad hoc (IBSS): ATIM