Wireless Multimedia Systems Fall, 2010 (Topic 7)

Professor Eric Hsiao-kuang Wu (hsiao@csie.ncu.edu.tw)

- Today's topic (

Mobility in IP Network

Suggested Reading:

Required Reading:

- [Bhagwat96] Pravin Bhagwat, Charles Perkins, and Satish Tripathi, “Network Layer Layer Mobility: An Architecture and Survey

- [Saha 2004] Debashis Saha, Amitava Mukherjee, Iti Saha Misra, Mohuya Chakraborty, “Mobility Support in IP: A survey of related protocols”, IEEE Network November/December 2004.

Network Layer Mobility: An Architecture and Survey

- TCP/IP : Internet Naming and Addressing

Internet Addressing (32-biy for IPv4, 128-bit for IPv6)

Naming: Name server responsible for mapping IP address and name

Hierarchical addressing scheme:

Network-id + host-id

Therefore, a mobile host must be associated with a new address when it moves

- The Mobility Problem

Name & address

Name: a location dependent identifier of a host

Address: a host’s point of attachment to the network

a. Mobility Problem: Directory Service View

difficulty:

a. DNS originally provide name lookup

b. DNS attempts t optimize the access cost ad not the update cost

c. DNS clients caches DNS records

b. Mobility Problem: Internet View

TCP identifier was identified by

<source IP address, source TCP port, destination IP address, destination TCP port>

In order to retain transport layer sessions, a mobile host’s address must be preserved regardless of its point of attachment to the network.

- Network-Layer Solution Architecture

Assumption:

Assume the rate of the change of location is slower than the time it takes for the mobile routing protocols

- a. Mobile host / Home Address / Home Network /d. Foreign Network

- b. Tow-Tier Addressing

forwarding address for routing directive

home address for an end-point identifier

virtually connected to its home.

- c. Architecture Components

- Forwarding Agent / Address Translation Agent

- g (forward address) -> (home address) will occur in FA

- f (home address) -> (forwarding address) will occur in ATA

- d. Location Update Protocol

- e. Packet Forward Operation

- f. Address Translation Mechanism

Mobile IP:

CH: Corresponding Host

HA: Home Agent

MH: Mobile Host

  - Acquire a IP from friendly foreign network

  - DHCP from foreign network

  - Acquire foreign agent’s IP address

(A) from CH to MH (through home agent)

f, g. Encapsulation(often called Tunneling)

If the mobile node moves again to another network attachment, it might cause packet loss. Higher layer internet protocol will ensure reliable packet delivery.

Foreign agent will de-capsulate the enclosed packet

(B) from MH to CH (direct to CH)

Illustration of Encapsulations:

Typical Example:

Security Issues:

(4) Mapping to Candidate Mobile Protocol, Some Solutions

  - Columbia Scheme

  - Mobile IP

  - Mobile IP with Route Optimization

When home agent forwards the packet, it could issue ICMP to inform CH that MH has moved to the new place.

Micro-mobility Management