Wireless Multimedia System

Professor Hsiao-kuang Wu (hsiao@csie.ncu.edu.tw)

Homework 3: (Due Dec 17  9:00 AM, 2008)

(Mobile IP)

1. Mobile IP (RFC 2002) is the current IETF standard for supporting mobility on the internet. (A) Explain what is the disadvantage to adopt enhanced DNS approach to solve the mobility problem? (B) Describe why mobile IP adopts two-tier addressing? (c) Explain what is meaning of f and g function? (D) What is the meaning of triangle routing? How to avoid the triangle routing to optimize the route? (E) Explain How IPv6 avoids triangle routing?

(Cellular Concept)

2. (A)  If a total of 25 MHz of bandwidth is allocated total particular FDD cellular telephone system which uses two 25 kHz simplex channels to provide full duplex voice and control channels, compute the number of channels available per cell if a system uses (1) 3-cell reuse (2) 7-cell reuse. (3) 12-cell reuse. (B) If a signal to interference ratio of 15 dB is required for satisfactory forward channel performance of a cellular system, what is the frequency reuse factor  (D/R) and cluster size (N) that should be used for maximum capacity if the path loss exponent is (a) n = 4, (b) n = 6 ? Assume that there are 6 co-channels cells in the first tier, and all of them are at the same distance from the mobile. Use suitable approximations. (Candidate Cluster sizes could be 3, 7, 12, 13).

(Channel Assignment & Handoff)

3. (A) A given radio spectrum (or bandwidth) can be divided into a set of disjoint or non-interfering radio channel. All such channels can be used simultaneously while maintaining an acceptable received radio signal. Channel allocation schemes can be divided into a number of different categories depending on the comparison basis. Describe FCA (Fixed Channel Allocation), DCA (Dynamic Channel Allocation) and HCA (Hybrid Channel Allocation). (B) Describe what is the meaning of Handoffs, intra-cell handoff, inter-cell handoff? In order to determine handoff initiations, several strategies have been proposed: Relative signal strength, Relative signal strength with threshold, Relative signal strength with hysteresis (plus optionally dwell timer). Explain the approaches.

(802.11 Power Saving Mode)

4. The IEEE 802.11 [23] standard recommends the following technique for power conservation. A mobile that wishes to conserve power may switch to sleep mode and inform the base station of this decision. The base station buffers packets received from the network that are destined for the sleeping mobile. The base station periodically transmits a beacon that contains information about such buffered packets. When the mobile wakes up, it listens for this beacon, and responds to the base station which then forwards the packets. This approach conserves power but results in additional delays at the mobile that may affect the quality of service (QoS).

(a) Decribe the difference between Active Mode and Power Saving Mode.

(b) How does Power Saving Mode Station know when to wait up to get the TIM (Traffic Indication Map)?

(c) Decribe is the purpose of TIM (Traffic Indication Map).

(d) How does Power Saving Mode Station to inform AP that he is ready to accept the buffered data?

(e) For BSS multicast services, how does AP transmit multicast or broadcast to all of the Stations if at least one of the stations are in power saving mode? (hint DTIM)

(Direct Sequence Spread Spectrum)

- (A) Direct Sequence Cellular system adopts universal frequency reuse policy. Explain what is universal frequency reuse policy? What is the advantage and disadvantage of this policy? (B) If W=1.25 MHz, R=9600 bps, and a minimum acceptable E/N is found to be 10 dB, determine the maximum number of users that can be supported in a single-cell CDMA system using omni-directional base station antennas and voice activity factor α = 3/8, K = 1/2, suppose the background noise is approximately neglected, where W/R is called the processing gain, (C) Explain why reverse link is vulnerable to the “near far” problem, and what is solution to maximize the system capacity? (d) Explain soft handoff and softer handoff?

Problem 6

(A) TCP is a reliable transport protocol tuned to perform well in traditional networks made up of links with low bit-error rates. Explain what are the slow start and congestion avoidance periods? (B) What is the problem for TCP to be carried over wireless environment? (c) Compare the following solutions (1) Split Connection Approach (2) Snoop Protocol (3) Westwood TCP.

Problem 7

An urban area has a population of two million residents. Three competing trunked mobile networks (systems A, B, and C) provide cellular service in this area. System A has 394 cells with 19 channels each, system B has 98 cells with 57 channels each, and system C has 49 cells, each with 100 channels. Find the number of users that can be supported at 2% blocking if each user averages two calls per hour at an average call duration of three minutes. Assuming that all three trunked systems are operated at maximum capacity, compute the percentage market penetration of each cellular provider.

(GOS= 0.02, C = 19, A = 12, GOS=0.02, C=57, A = 45, GOS= 0.02, C= 100, A = 88.)