1.

(1) Ericsson, Nokia, IBM, Toshiba, and Intel publish the Version 1.0of the specification in July 1999. Over 1000 companies have signed as adopters of the technology.

(2) Bluetooth and the 802.11 standards can peacefully coexist because each was designed for a distinct purpose. The 802.11 standards are specifically designed for running WLANs that create a network of computers and connect users to the Internet. Bluetooth, on the other hand, is designed to allow portable devices to communicate with each other. However, many agree that Bluetooth can be used in an office or classroom to connect mobile devices in the same space that a WLAN is running to create a computer network.

Both WLAN and bluetooth technologies are popular wireless connections for voice and data communications. the two technologies use the same frequency spectrum, which must be shared effectively for both technologies to be used at the same time. An advanced Packet Traffic Arbitration (PTA) algorithm with voice packet prioritization ensures seamless collaboration between Bluetooth and WLAN and excellent voice/audio quality. Adaptive Frequency Hopping (AFH) capability to actively avoid WLAN frequency channels that are in use.

(3) DSA maximizes the bandwidth utilization and minimizes latency within a piconet. DSA scheme enables for not only slave-to-slave communication but also serves as multi-device communication (MDC), hence emulating a multicast-like communication within the piconet.

(4) A single time slot in the Bluetooth system lasts 625us. It can be though of as the time it takes to send one packet from one Bluetooth device to another.

(5) The communication channel can support both data (asynchronous) and voice (synchronous) communications with a total bandwidth of 1 Mb/sec. The supported channel configurations are as follows:

| Configuration | Max. Data Rate Upstream | Max. Data Rate Downstream |
| --- | --- | --- |
| 3 Simultaneous Voice Channels | 64 kb/sec X 3 channels | 64 kb/sec X 3 channels |
| Symmetric Data | 433.9 kb/sec | 433.9 kb/sec |
| Asymmetric Data | 723.2 kb/sec or 57.6 kb/sec | 57.6 kb/sec or 723.2 kb/sec |

(6) Bluetooth radios communicate using a time division duplex discipline (TDD). Because more than two devices share the piconet medium, the access technique is TDMA. Thus, piconet access can be characterized as FH-TDD-TDMA.

(7) Occasionally, two piconets will use the same physical channel during the same time slot, causing a collision and lost data. However, because this will happen infrequently, it is readily accommodated with forward error correction and error detection/ARQ techniques. Thus, a form of CDMA is achieved between devices on different piconets in the same scatternet; this is referred to as FH-CDMA.

2.

(A)(1) (channels)

(2) (channels)

(3) (channels)

(B)(a)

(b)

3.

(A) FCA: assign a number of channels to each cell permanently according to some reuse pattern.

DCA: all channels are placed in a pool and dynamically assigned to a new call to satisfy minimum CIR.

HCA: a combination of fixed and dynamic channel allocation schemes, with the channels divided into fixed and dynamic sets. This means that each cell is given a fixed number of channels that is exclusively used by the cell. Request for a channel from the dynamic set is initiated only when a cell has exhausted using all its channels in the fixed set.

(B) Handoff: change the radio channel due to the radio link degradation or channel reorder.

Intra-cell handoff: change channel in the same cell.

Inter-cell handoff: user moves to a new cell, so the channel must be reallocated.

Relative signal strength: always choose the channel with the strongest signal.

Relative signal strength with threshold: when current signal is below the receiver threshold and signal from another station is higher than handoff threshold, handoff.

Relative signal strength with hysteresis: handoff when the signal is lower than a near station for a period of time.

4.

(a) active mode : STA 可以在任何時間接收frame。在active mode中，STA必須隨時在awake state。

power save mode: STA每隔一段時間去聽selected beacons，若beacon中的TIM element指示有MSDU要傳來，則必須回PS-Poll frame，在PS mode中，STA大部分時間是在Doze state, 而在接收selected beacons、 broadcast or multicast transmission與傳送時，進入awake state。

(b) 在PS mode的STA應該依據STA的ListenInterval與ReceiveDTIMs parameters periodically 去聽beacon(TIM包含在beacon中)。

(c) TIM可以告訴STA，AP是否有要傳給它的buffered data。若有，STA就必須保持在awake state，否則它可以回到 dozen state進入power save mode 節省power，直到下一次聽beacon的時間再wake up。

(d) power saving mode station 由beacon中知道AP有自己的buffered data，則由response AP一個PS-Poll frame告知AP 他已準備好要接收buffered data。

(e) 若有任何一STA在PS mode, AP會buffer 所有broadcast與multicast MSDUs, 直到下一個包含delivery TIM(DTIM)的beacon發送時，緊接著beacon把這些MSDUs 發送給所有的STA.

5.

(A) universal frequency reuse policy: 一個cell內所使用的frequency，在隔壁cell就可以馬上被reuse，不需要區格多個cell之後才再利用。

advantage:

- If traffic at the location increases, the introduction of new cell will be less restricted compared with FDMA or TDMA.

- Universal frequency reuse turns out to be beneficially affects or improves the capacity of the system.

- Avoids the complicated issue of frequency-management planning when additional cells are introduced.

- Applies to all users in the assigned spectrum or channel, to all cell sites, and to all media, terrestrial and satellite-both geostationary and low earth orbit.

- With CDMA, seamless handover between media becomes possible.

- enables the new function soft handover

disadvantage:

- Creates additional interference when increase in the effective receiving angle enlarges overlapping region and causes more interference to the user.

- Near-far problem.

(B)

(C)(i) The goal in CDMA systems is to assure that all mobiles achieve the same received power levels at the Base Station. The reverse link is vulnerable to the near-far problem because of the strongest (nearby) reverse link can capture the intended receiver but weaker (far away) reverse link get ignored by the receiver. In order to minimize the Reverse Link Near-Far problem, mobiles that are closer to the Base Station must transmit less power than mobiles that are further away from the Base Station. For Example, DS-CDMA is mitigating the problem by using a combination of open-loop and closed-loop power control.

(ii) CDMA is interference limited. Therefore reducing interference is also most important in increasing the capacity. The power control reduced the average mobile transmitted powers as well.

(D) Soft handoff: A Mobile Station is communicating simultaneously with the prior Base Station as well as the new BS. Such a scheme, just for some short duration of time, is called soft handoff or make before break.

Softer handoff: Similar to soft handoff, softer handoff is the soft handoff between two sectors of the same cell. For a perfect sectorized antenna pattern, softer handoff cannot be applied. In practice, the antenna patterns do not fit the sector area perfectly, and there is an overlapping of the two antenna patterns between the sectors. The overlapping of the sector antenna patterns generates additional interference on both the reverse and forward links.